## Slide 1
CONTINUUM
WORKSHOP-2
Introduction to OpAmps

## Slide 2: WHAT IS DIODE?
Electronic devices created by bringing together a p-type and n-type region within the same semiconductor lattice. Used for rectifiers, LED etc. It is represented by symbol
2

## Slide 3: Biasing of Diode
4
Forward Bias : Connect positive of the Diode to positive of supply…negative of Diode to negative of supply
Reverse Bias: Connect positive of the Diode to negative of supply…negative of diode to positive of supply.

## Slide 4: I-V characteristics of Ideal diode

## Slide 5: Characteristics of Ideal Diode
» Conducts in one direction.
» Conduct current when “Forward Biased” ( Zero resistance/Short circuit)
» Do not conduct when “Reverse Biased”
(Infinite resistance/Open circuit)

## Slide 6: I-V characteristics of a practical diode

## Slide 7: I-V Characteristics

## Slide 8: Half-wave Rectification
» Simplest process used to convert ac to dc.
» A diode is used to clip the input signal excursions of one polarity to zero.

## Slide 9: Operational Amplifiers
10
_
+

## Slide 11: Operational Amplifiers
Usually Called Op Amps
An amplifier is a device that accepts a varying input signal and produces a similar output signal with a larger amplitude.
Usually connected so part of the output is fed back to the input. (Feedback Loop)
Most Op Amps behave like voltage amplifiers. They take an input voltage and output a scaled version.
The name “operational amplifier” comes from the fact that they were originally used to perform mathematical operations such as integration and differentiation..

## Slide 12: Operational Amplifiers
Op amps can perform operations of:-
Adding signals
Subtracting signals
Integrating signals
Differentiating signals
The applications of operational amplifiers ( shortened to op amp ) have grown beyond those listed above.
For example : Temperature sensor, Audio amplifiers, Active filters

## Slide 13: Pin Diagram of LM 741

## Slide 14: Operational Amplifiers
A model of the op amp, with respect to the symbol
Vo= AVd

## Slide 15: Working circuit diagram of op amp.

## Slide 16: Open Circuit Output Voltage
The voltage produced by the dependent voltage source inside the op amp is limited by the voltage applied to the positive and negative rails.

## Slide 17: Voltage Transfer Characteristic

## Slide 18: Example: Voltage Comparator
.
When V1 is equal to V2, Vo = 0V When V1 is smaller than V2, Vo = V+. When V1 is larger than V2, Vo = V-.

## Slide 19: Electronic Response
Given how an op amp functions, what do you expect Vo to
be if v2 = 5V, A=10 when:
Vs = 0V?
Vs = 5V?
Vs = 6V?

## Slide 20: Ideal Op Amp
Ri=∞Ω
Hence i1=i2=0A
Ro=0Ω
i1 = 0
i2 = 0

## Slide 21: FEEDBACK IN CIRCUITS
Negative feedback
Positive feedback

## Slide 22: Why Negative Feedback?
Gain of op amp (open loop gain) is of the order of 10^6 which is enough to drive the op amp into saturation.
We want the operation of op amp to be in the linear region for proper amplification purpose.
So to reduce gain we apply negative feedback.

## Slide 23: Why positive feedback?
32
» When we want the amplifier to work in saturation only then we use positive feedback.
» It decreases the bandwidth and increases the overall amplification.
» Gpf= A/(1-Aβ)

## Slide 24: Negative Feedback Equation
We see that the effect of the negative feedback is to reduce the gain by the factor of: 1 + βG.
This factor is called the “feedback factor” or “amount of feedback” and is often specified in decibels (dB) by the relationship of 20 log (1+ βG).

## Slide 25: Applications of Negative Feedback:-
Inverting Amplifier
Non-Inverting Amplifier
Adder , Subtractor
Log , Antilog
Integrator, Differentiator
Temperature sensor
Instrumentation amplifier
Active Filters

## Slide 26: Virtual Short Circuit in Ideal OpAmp

## Slide 27: Inverting amplifier:
Writing a nodal equation at (a) gives;
With Vi = 0 we have;

## Slide 28: Non-inverting Amplifier
Closed-loop voltage gain

## Slide 29: Summing Amplifier
If R1 = R2 = Rfb then,
Therefore, we can add signals with an op amp.

## Slide 30: Logarithmic Amplifier
Logarithmic amplifier gives the output proportional to the logarithm of input signal.
If Vi is the input signal then the output is
Vo = K*ln(Vi)
where K is gain of logarithmic amplifier.

## Slide 31: Questions
33

## Slide 32: Questions
37

## Slide 33: Questions
34

## Slide 35: Questions
35

## Slide 37: Alternate proof for virtual short circuit in Ideal OpAmp
In ideal OpAmp, Ri=∞Ω (approx), and currents in input terminals are zero, then potential difference between the terminals Vd=0V, hence V1=V2.

## Slide 38: Thank You! ☺
Contact us:
Mohit Shringi: 6377566533
Rishabh Borad: 9450336209
P. Shyam Prasad: 9494146711